## Slide 1
Longitudinal Trajectories of Resting-State qEEG Biomarkers in
Cognitively Normal Older Adults Stratified by Amyloid-PET Status
Korean Biomedical Engineering
2025.12.01

## Slide 2
Dementia burden globally is accelerating—public health priority
Amyloid-β accumulates 15–20 years before cognitive symptoms (preclinical AD)
Current diagnostics: PET, CSF are expensive, invasive, and impractical for large-scale screening
The opportunity: EEG is non-invasive, portable, affordable, and captures real brain activity
Gaps: Most EEG studies are cross-sectional; repeated-measure longitudinal EEG in cognitively impairment is lacking. Especially, no existing longitudinal study on normal Aβ+ vs Aβ− cohorts.
Background

## Slide 3
Primary aim:
Characterize longitudinal trajectories of resting qEEG markers and test if Aβ+ and Aβ− cognitively normal older adults show different rates of neurophysiological change over time.
Specific Objectives:
Compare baseline qEEG profiles (power, ratios, asymmetry) between Aβ− and Aβ+
Model annual rate of change (slope) in qEEG markers using mixed-effects models
Identify earliest-diverging EEG biomarkers as candidate surrogate endpoints
Aims & Objectives

## Slide 4
Design: Prospective longitudinal observational cohort study
Participants:
- Cognitively normal (CN) older adults, age ≥ 55
- Amyloid-PET positive (Aβ+) vs. negative (Aβ−)
- ≥ 2 valid EEG sessions over multi-year follow-up
Data Collection:
- Baseline: MMSE, SNSB cognitive battery, amyloid-PET
- EEG: Resting-state (eyes-closed, 5–10 min) at baseline and annual follow-ups
- Optional future: Sensory/Attention tasks
Study Design

## Slide 5
Electrode Setup (10–20 system):
- Frontal: Fp1/2, F3/4, Fz
- Central: C3/4, Cz
- Parietal/Occipital: P3/4, Pz, O1/2
Reference Strategy:
- Initial: Linked-ear or mastoid reference
- Re-reference to linked mastoids (midline components) or average reference (topographic mapping)
- Consistent referencing across all visits for longitudinal accuracy
Sampling & Filtering:
- Sampling rate: 250–512 Hz
- Band-pass filter: 0.5–45 Hz
- Notch filter: 50/60 Hz (line noise)
EEG Recording & Preprocessing Strategy

## Slide 6
Artifact Types (per Prof. Kim's framework):
- Ocular: Eye blinks, saccades → Independent component analysis removal
- Muscle: Jaw, neck tension → EMG thresholding
- Technical: Electrode pops, line noise → interpolation/filtering
- Physiological: ECG, respiration → frequency-specific rejection
Quality ontrol Steps:
- Bad-channel interpolation
- ICA for ocular/muscle components
- Epoch rejection: amplitude thresholds, kurtosis
- Minimum clean data requirement: ≥ 3–5 minutes per visit
- Per-subject quality flag: outlier_extreme (|z| > 3)
Signal Cleaning & quality control

## Slide 7
Bands
Delta (0.5–4 Hz): Slowing marker (AD)
Theta (4–8 Hz): Memory, attention; ↑ in MCI/AD
Alpha (8–13 Hz): Normal awake state; ↓ in AD
Beta (13–30 Hz): Alertness, focus; ↓ in AD
Gamma (30–45 Hz) Higher cognition; task-dependent
Spectral Ratios:
TBR (Theta/Beta): Attention marker; higher = more slowing
ABR (Alpha/Beta):** Neurophysiological slowing index
SPR ([Delta+Theta]/[Alpha+Beta]): Global slow-power ratio; sensitive to AD progression
qEEG Features: Band Power & Spectral Ratios

## Slide 8
Asymmetry Indices:
FAA (Frontal Alpha Asymmetry): ln(F4_α) − ln(F3_α)
Reflects lateralized prefrontal engagement
Altered in depression, mild cognitive impairment
FBA (Frontal Beta Asymmetry): ln(F4_β) − ln(F3_β)
Peak Frequency (Fpeak):
- Alpha peak at posterior sites (Pz, Oz)
- Higher frequency = better cognitive status; Lower = aging/slowing
- "Brain age" estimate from Fpeak
Median Frequency (MEF 4–50 Hz):
- Global slowing marker
- Known to decrease with age and dementia
Advanced Markers: Asymmetry & Peak Frequency

## Slide 9
Data Cleaning & Integration
Import raw EEG and clinical/PET data
Parse visit dates, derive elapsed_years from first EEG visit
Standardize IDs, demographics, diagnosis labels
EEG QC & Feature Extraction
Apply preprocessing pipeline (referencing, filtering, artifact removal, epoching)
Compute PSD (Welch), integrate band powers, compute ratios/asymmetry
Flag outliers; create "outlier-clean" dataset
Longitudinal Dataset Assembly
Merge cleaned EEG features with clinical/PET data
Restrict to CN participants with ≥2 valid EEG visits, AGE ≥ 55
Define Amyloid_Status (Aβ− reference, Aβ+)
MICE imputation for cognitive scores only
Longitudinal Data Assembly & Preprocessing

## Slide 10
Linear Mixed-Effects Modeling
Model specification: EEG marker ~ elapsed_years × Amyloidstatus + Covariat factors + (1 + elapsed_years | object ID)
Fitted using lmerTest::lmer() for all EEG markers
Random intercepts + random slopes per subject to capture individual heterogeneity
Statistical Inference Strategy
Test: Likelihood Ratio Test (LRT) comparing full vs reduced models (no interaction term) & Wald test for interaction coefficients (descriptive)
Effect size: Cohen's d from standardized slope differences
Reporting: Annual slopes per group, 95% CI, both LRT and Wald p-values
Trajectory Models

## Slide 11
Hypothesis:
Aβ+ CN will show faster annual slowing (↑ theta/SPR slope, ↓ alpha/beta/Fpeak slopes)
Aβ− CN will show minimal or stable qEEG trajectories
Clinical Implications:
Serial qEEG could identify preclinical individuals most likely to progress
Cost-effective alternative for frequent monitoring vs. repeated PET
Anticipated Findings & Clinical Meaning

## Slide 12
THANK YOU FOR YOUR ATTENTION